## Slide 1: Hardware implementation and Demonstration

## Slide 2: Synapse RF26X
We started off with Synapse RF26X
    10-bit ADC
    Up to 2 Mbps Data Rate
    4K internal EEPROM
    128k flash (58k free for over-the-air uploaded user apps)
    ATmega128RFA1 single-chip AVR microcontroller
But Floating Points were not supported

## Slide 3: CC2530 ZDK
So we chose another module to work with that supported floating points: CC2530 ZigBee Network Processor Mini Development Kit
    2.4-GHz IEEE 802.15.4 Compliant RF Transceiver
    High-Performance and Low-Power 8051 Microcontroller Core
    In-system programmable flash memory 32-KB
    1-KB RAM
    12-Bit ADC
    Internal temperature sensor
    Light sensor SFH 5711
    Accelerometer CMA3000-D0X
    Floating points supported

## Slide 4: Sensor Motes
Many beginner level examples could be found on the internet regarding this module
We started learning through those simple examples and successively moved on to more complex tasks
First of all we interfaced and calibrated the on-chip sensors for: light, temperature, battery level and accelerometer
Then we wrote a simple routine that would communicate the readings from the end node to the coordinator node

## Slide 5: Sensor Motes
We made a state machine that would only communicate with the coordinator node once the local event has occurred
Using this topology, we were able to reduce communication overhead and Power Consumption

## Slide 6
Idle state
Network Info State
Measurements Acquisition and Outlier Detection State
Event Detection and Info Message Sending State
Default
(if something goes wrong)
ZNP Startup State

## Slide 7: Limitations
Memory Constraints
    Resetting of the Nodes, due to memory overflow
    Small training data set
Computational Limitation
    Only able to process two attributes, since no matrix operations support
    Problem in Event Identification
Sensor stability
    Value of luminosity fluctuates

## Slide 8: Online ellipsoidal Clustering WHY?
The prime reason for selecting the online method for outlier detection was the limited memory that we had to work with
Other methods require way more memory than the online ellipsoidal clustering method
Our choice of the algorithm was correct; we successfully detected outliers
The next step was the detection of event for which we implemented our proposed algorithm presented by bilal

## Slide 9: Event detection
After the detection of local events on end nodes we moved on to global event detection
For declaring global event all end nodes communicate their outliers to the coordinator node once local event has been declared
The coordinator node calculates a similarity parameter that would indicate the similarity between the outliers that caused events on different nodes: Bhattacharya coefficient
To get a more precise value of Bhattacharya coefficient (and to make a visual simulation), we interfaced the coordinator node with Matlab